## Slide 1: Work Progress
By: Abdur Rehman

## Slide 2: Visualizing the Inputs and Outputs
The control inputs are the feed F and the heat flow:

## Slide 3
The four states are concentration of reactant A (CA), the concentration of reactant B (CB), the temperature inside the reactor (TR) and the temperature of the cooling jacket (TK):

## Slide 4: Custom Inputs and Outputs Function
  The idea of this custom function is to take the random Input, used the Output generated from the DO_MPC simulator and assign the Input/Output Delays for the NARX Model and receive the Training, Testing, Input and Output Layers in the form of: X_train, X_test, y_train, y_test, input_layers, output_layers

## Slide 5: Callbacks
  To efficiently used the Hyperparameter Tuning, callbacks come in handy. It can perform various tedious actions at various stages of the training.
  Some of the Callbacks used are the following: EarlyStopping, CSVLogger, TerminateOnNaN, TensorBoard

## Slide 6: Keras-Tuner: Hyperparameter Optimization Framework
Tune The Model Architecture:
  The first thing we need to do is writing a function, which returns a compiled Keras model. It takes an argument hp for defining the hyperparameters while building the model.
  The parameters expected to be tuned:
    Delay Size in the Input and the Output
      input_delay_size = hp.Int("input_delay_size", 2, 20, step=1)
    Number Of Hidden Layers
      range(hp.Int('hidden_layers', 2, 25))
    Number Of Neurons
      units=hp.Int('units_nodes_' + str(i), min_value=32, max_value=256, step=8)
    Activation Functions
      activations=hp.Choice('activation_', ["relu", "tanh", "sigmoid"])
      activation=activations
    Learning Rate
      hp.Choice('learning_rate', [1e-1, 1e-2])
Optimizers Used ADAM:
  optimizer=tf.keras.optimizers.Adam
Metrices Considered:
  metrics=['mean_squared_error', 'mean_absolute_error', 'mean_absolute_percentage_error’, tf.keras.metrics.RootMeanSquaredError()]
Loss: 'mean_absolute_error'

## Slide 7: Results 1:
tuner.results_summary()
  Best mean_absolute_error So Far: 0.017436451092362405
  Total elapsed time: 00h 09m 41s
best_hp.values
{'input_delay_size': 16, 'activation_': 'relu', 'hidden_layers': 2, 'units_nodes_0': 72, 'units_nodes_1': 184, 'learning_rate': 0.01, 'units_nodes_2': 136, 'units_nodes_3': 104, 'units_nodes_4': 136, 'units_nodes_5': 120, 'shuffle': True, 'units_nodes_6': 88, 'units_nodes_7': 256, 'units_nodes_8': 216, 'units_nodes_9': 80, 'units_nodes_10': 40, 'units_nodes_11': 256, 'units_nodes_12': 216, 'units_nodes_13': 120, 'units_nodes_14': 216, 'units_nodes_15': 88, 'units_nodes_16': 192, 'units_nodes_17': 64, 'units_nodes_18': 232, 'units_nodes_19': 144, 'units_nodes_20': 216}
History TEST | 
loss | 0.014079165644943714
mean_absolute_error | 014079165644943714
mean_squared_error | 0.0011004337575286627
root_mean_squared_error | 0.033172786235809326
History TRAIN | 
loss | 0.0131768099963665
mean_absolute_error | 0.0131768099963665
mean_squared_error | 0.0009960528695955873
root_mean_squared_error | 0.03156030550599098

## Slide 8
Model: "sequential_1"
_________________________________________________________________
Layer (type) Output Shape Param #
=================================================================
flatten_1 (Flatten) (None, 96) 0
dense_5 (Dense) (None, 72) 6984
dense_6 (Dense) (None, 184) 13432
dense_7 (Dense) (None, 4) 740
=================================================================
Total params: 21,156
Trainable params: 21,156
Non-trainable params: 0
_________________________________________________________________

## Slide 15: CLOSED LOOP SIMULATION

## Slide 17: DEMONSTRATION
STEP II: Take the entire row and feed it to the Neural Network (X_K)
STEP I: Creation of a Dummy Array to feed the Input and run the Closed Loop Simulation
  Needs to make sure the model and the inputs are built on the same parameters
    inputs = X_train_HyperParametersModel
  Finding out the rows and columns for the closed loop simulation array
    row_closed_loop, column_closed_loop = inputs.shape
  Creation of the Closed Loop array
    closed_loop_NParray = np.zeros((row_closed_loop, column_closed_loop))
  Setting up the initail Valuse for the closed loop simulation from the inputs[0] to dummy variable [0]
    dummy_0 = inputs.loc[0]
    closed_loop_NParray[0] = dummy_0

## Slide 18
STEP III: Taking the entire row and feeding it to the Neural Network (X_K)
  states_from_the_model = history_model.predict(states_from_the_model)
STEP IV: Taking the entire row and feeding it to the Neural Network (X_K)
  Shifting all of the STATES based on the delay (X_K-1)
  Completing the Entire row and shifting it to the next row …

## Slide 19
STEP V: Using the Neural Network Model, assigning the first row to the model and fitting it in the second row
STEP VI: Repeating the shifting procedure for the Inputs
STEP VII: Inserting the New Input from the Simulated Data